## Slide 1: AVEKSHA: A Hardware-Software Approach for Non-intrusive Tracing and Profiling of Wireless Embedded Systems
Current approaches to debugging deployed Wireless Sensor Networks (WSN) can be improved
  Software: affects application timing and is OS specific
  Hardware: bench debuggers not suitable for deployment
How can we perform tracing and profiling that is
  Non-intrusive
  Able to trace with high spatial and temporal granularity
  Low energy
  Low cost
  Easy to integrate and deploy
Problem Statement
Solution Approach
JTAG is a protocol
  TDO data output
  TDI data input
  TMS select mode
  TCK clock
The MSP430 comes with a JTAG accessible debug module that provides
  Processor emulation
  Breakpoint and watchpoint triggers
  State-storage (data and address bus) on trigger
What is JTAG?
Design
Bug Fixed
Reference
M. Tancreti, M. S. Hossain, S. Bagchi, V. Raghunathan, “AVEKSHA: A Hardware-Software Approach for Non-intrusive Tracing and Profiling of Wireless Embedded Systems,” in Proceedings of the 9th ACM Conference on Embedded Networked Sensor Systems, SenSys ’11, ACM, 2011.
AVEKSHA is a hardware/software approach
Exploit the JTAG debug module
  Comes free on every chip (e.g. MSP430 EEM)
  Asynchronous with the main processor
  Has advanced features: complex breakpoints and watchpoints, triggered state-storage
Approach
  Poll processor state over JTAG
  Filter for important events
  Tag event with energy reading (may not be casually related)
  Store to flash or stream over USB
School of Electrical and Computer Engineering, Purdue University
Matthew Tancreti, Mohammad Sajjad Hossain, Saurabh Bagchi, Vijay Raghunathan
What We Built: The Telos Debug Board
Reverse engineered an important JTAG protocol (MSP430)
  A common low-power sensor network MCU
  Profiling and tracing not just for Arm CoreSight class chips
Designed a JTAG debugger suitable for deployed WSNs
  Non-intrusive (does not change timing)
  OS/compiler agnostic
  Low power
  No significant hardware modification to mote
  Easy to deploy (does not need to be programed in advance)
Verified our design
  Tracing and profiling in TinyOS and Contiki
  Found resource consuming bug in TinyOS low-power-listening radio stack
Our Contributions
MCU for initialization and configuration
FPGA for high speed polling and filtering pipeline
Connects to mote IO and JTAG interfaces
Provides power to mote from battery or USB
PC polling down to granularity of 7 mote cycles
Usually enough to catch every function transition
Knowledge of call graph required to convert polled PC data into profile
Profiling With PC Polling
Methods for Tracing and Profiling Applications
Acknowledgements
This work was supported in part by NSF grants CNS- 0953468, ECCS-0925851, and CNS-0716271. The views expressed represent those of the authors and do not necessarily reflect the views of the sponsoring agency.
Watchpoint polling
  Triggers can be set for generic events e.g. function call and return
  A nop insturction can be used to by the programmer to specify arbitrary trigger locations in code
PC polling
  Poll the PC counter
  Binary search to find code block that PC counter belongs
Speed of Polling
Watchpoint Polling
  TDB polls buffer at rate of 30.5us
  Cannot exceed burst of 8 events in 976 mote cycles
  Suitable for tasks and states, but not function call granularity
PC Polling
  Cannot do PC polling and watchpoint triggers together
  1 PC poll takes 7 mote cycles
  Suitable for function call granularity
MSP430 has 8 triggers slots that are conditions based on
  data or address bus (MDB/MAB)
  read, write, or instruction fetch (-R/-W/-F)
  Combination of triggers
8 entry circular state-storage captures address and data bus after a trigger is fired
OS Agnostic
We can change from debugging TinyOS tasks to Contiki processes without reprogramming the board
FPGA for polling JTAG and filtering events
  Would require MCU at much higher clock frequency
MCU for initialization and coordination
USB connectivity to stream data to host PC
Goal is to poll JTAG at maximum possible speed
For PC polling pipeline stages are: poll PC address, binary search for function pointer, filter: is this a new function, output buffer
PowerCycleP Re-post Bug
Accidentally discovered bug when tracing all tasks
PowerCycleP_startRadio re-posts itself when SubControl_start() != SUCCESS
When radio is already started SubControl__start() = EALREADY
Re-post could be permanent with following hypothetical code
Simple fix
Now patched in TinyOS repository (see issue 51)